## Slide 1: Efficient Processing of Deep Neural Networks: A Tutorial and Survey

## Slide 2: Ways of Speeding up Convolution
FFT
Stassen
Winograd
Different algorithms might be used for different layer shapes and sizes(FFT – greater than 5*5 Winograd for filters 3*3 and below)

## Slide 3: Dataflow
Weight stationary
Output stationary
No local reuse
Row Stationary

## Slide 4
Two problems in data flow
Fixed-size PE array - different layer shapes
Fixed design - data in different patterns
Two solutions
Replication – do not use the entire PE array
Folding – split the large size into several segments

## Slide 5: Near-Data Processing
- processing-in-memory / logic-in-memory
--mixed-signal circuit design and advanced memory technologies
Problems: reduced precision and overhead cost for ADC & DAC

## Slide 6
Memory technologies
A. DRAM -- bring memory to the compute
– eDRAM (on chip) : higher bandwidth and lower latency
lower density and higher cost
- TSV(lower capacitance than typical off-chip interconnects) 3-D memory HMC(High Memory Cube) HBM(High Bandwidth Memory)

## Slide 7
B. SRAM – bring compute to memory
C. Non-volatile Resistive Memories
PCM ReRAM CBRAM STTMRAM
D. Sensor perform the computation as close as possible to the sensor -- before ADC within sensor

## Slide 8: Co-Design of DNN Models and Hardware
Two General Approaches
1. Reduce precision of operations and operands
2. Reduce number of operations and model size

## Slide 9
A. Reduce Precision
Reducing the number of levels, and thus the bits
Reduce weights rather than activations
Reduce inference rather than training
1. Linear quantization
First, float -> fixed -- reduce the energy and area for the memory
* binary nets BC BNN BWN; TWN(Ternary Weights Nets) TTQ

## Slide 10
2. Non-linear quantization
1) log domain quantization
2) learned quantization or weight sharing (weight index log base 2)
weight sharing approach does not reduce the precision of the MAC computation itself and only reduces the weight storage requirement

## Slide 11
B. Reduce Number of Operations and Model Size
1) Exploiting Activation Statistics
RELU sparsity – compression, zero-skipping
2) Network Prunning
a large amount of the weights in a network are redundant and can be removed
CSR CSC

## Slide 12
3) Compact Networks Architecture
replace a large filter with a series of smaller filters
4) Knowledge Distillation
Teacher DNN?

## Slide 13: Benchmarking Metrics
Accuracy/robustness
Energy and power
High throughput
Low latency
Hardware cost

## Slide 14
A. Metrics for DBB Models
The accuracy of the model
The network architecture
The number of weights
The number of MACs

## Slide 15
B. Metrics for DNN Hardware
The power and energy consumption of the design
The latency and throughput
The cost of the chip